## Slide 1: ALIM Guide for asset information Managers
Michel Böhms

## Slide 2: overview
01. ALIM introduction
02. Planning for alim
03. Defining for ALIM
04. Implementing ALIM in software
05. Using ALIM in practice
06. Quick guide

## Slide 3: 01. ALIM introduction
Background
Definition
Purpose
Guide

## Slide 4: 01 ALIM Introduction
Big challenges In the built environment
Climate adaptation, Energy transition
Aging infrastructures
Pollution, CO2, Nitrogen issues
Housing shortage
Subsidence, gas-related earthquakes
Looming electrical/gas power shortages
The right “Digitalisation” is an important part of the solution
Within Digitalisation the right “Information Management” is key
background

## Slide 5: 01 ALIM Introduction
However, today’s information managers are confronted with a lot of data complexity if not data chaos
  Requirement specs, BIM data, GIS data, ERP data, measurement data, documents, …
  All having their own particular data formats and data structures (software-native or partial standard)
  Hampering internal and external communication and reuse
Resulting in suboptimal Information Management, hence suboptimal asset management and even suboptimal the asset’s operational utilization
We think our Asset Life-cycle Information Management (ALIM) approach can help out!
background

## Slide 6: 01. ALIM introduction
The term ALIM stands for Asset Lifecycle Information Management, referring to an approach for:
  The future proof modelling and linking of all relevant asset information from multiple perspectives, by multiple stakeholders/data source holders, from the asset’s inception till its end of life
  Covering the whole asset information life-cycle from creation till deletion
  In a, as much as possible, semantic, that is software-interpretable, way, reusing as much as “semantics” already out there
  Resulting in networks of complementing/strengthening information sets and information models
  Integrating existing software functionalities via standard data I/O, translators/convertors, Application Programming Interfaces (APIs), Query Languages etc.
          Future proof: based on open standards where possible, independent of any specific software vendor:
            Operationally FAIR: information becomes findable, accessible, interoperable and reusable keeping the data at its single source of truth (SSoT) also providing separation of concerns (SoC)
            Tactically Flexible: adaptable & extendable
            Strategically Innovative: ready for new software (web) services and advanced levels of automation (workflows)
definition

## Slide 7: 01. ALIM introduction
Improving project management (program/design/build) & asset management (operate)
… ultimately, improving the assets utilization:
  Better quality asset services (“for the people”), like
    - Improved structural integrity/safety
    - New transport options (platooning)
  Less asset operational costs (“for prosperity”)
    - Less failure cost
  Better for the environment (“for the planet”)
    - Improved durability & circularity
All by improved:
Information alignment
Information exchange & sharing
Information integration
All needing:
Information Modelling & Linking
purpose

## Slide 8: 01. ALIM introduction
ALIM is needed in practice but it is a complex, multi-facetted topic
Need for guidance for information managers to apply the ALIM approach in their organization
Hence this ALIM Guide for Information Managers!
Taking the information manager through ALIM’s own lifecycle!
  Step by step, introducing the relevant fora and topics out there at the right time
ALIM Life cycle
  Programming (planning) for ALIM
  Designing (Defining) for ALIM
  Building (Implementing) ALIM (in software)
  Operating (Using) ALIM
guide

## Slide 9: what is an Asset?
Any part of the Built Environment
  Buildings (residential, offices, factories, hospitals, …)
  Infrastructures (roads, rails, powerlines, bridges, tunnels, dikes, sluices, …)
  Process Plants (chemical plants, power plants, …)
  Maritime structures (wind turbines, offshore platforms, …)
  Or any complex combination of them: city, airport, harbour, …
  Or any part of them: systems, elements, parts, components and materials

## Slide 10: what is an Asset?
Assets can be Make or Buy
Products are special kinds of assets
Note …

## Slide 11: what is a life-cycle?
Programming (asset as required/allowed by client, law & regulation or sector)
Design (asset as designed)
Build (asset as constructed)
Operate (asset as in use) & maintain, renovate or repurpose, until its end of life: demolish, recycle & reuse
Maintenance: re-build
Renovation: re-design and re-build
Repurposing: re-program, re-design and rebuild
For every life-cycle phase we can have a supply-chain
  Example in the build phase: Client > Contractor <> Sub-contractor <> Supplier <> Manufacturer
  Related to the asset’s breakdown structure or “typical decomposition”

## Slide 12: what is a life-cycle?
Life cycle versus supply chain
Program
Design
Build
End of Life
Built Environment
Complex Asset
Asset
Element
Part
Component
Asset Network / Asset Collection
Asset supply chain / Asset breakdown
Start of Life
Material
Operate

## Slide 13: what is information?
Information sets, having some format that can be imported/exported or being accessible (“syntax” respectively “data access mechanism”)
Information models, giving the data sets meaning (“semantics”)
  Think: schemas, ontologies, OTLs, vocabularies, dictionaries & thesauri
Knowledge Models, giving, on their turn, information models (more) meaning
Link sets, interconnecting information sets or information models
Meta-information, information about information sets, information models, knowledge models and link sets. or their elements (up to triples)
Structured, for software-processing
  for data sets:
    - semantic (having an explicit data model) for software-interpretation or
    - non-semantic (“having no explicit data model) for human interpretation
Unstructured (“documents/files”) for human processing & interpretation
Typical situation is “Hybrid”: mix of documents, non-semantic and semantic information

## Slide 14: what is information?
ALIM is an umbrella concept for
  Building Information Modelling (BIM)
  Geospatial Information Systems (GIS)*
  Systems Engineering (SE)
  Monitoring Data coming from sensors & Control Data going to actuators (M&C)
    - often related to the Internet of Things (IoT) when sensors/actuators are web-based
  Electronic Document Management (EDM)
* Note: Better Geospatial Information Modelling (GIM) but not used in practice…sometimes GEO

## Slide 15: what is modelling?
Definition: information sets, and information models: like ontology/object type library
Storage: files, databases, documents, …
Transformation
  Format (“syntax”) translation
  Meaning (“semantic”) conversion
  Like import/export (download/upload in a web environment)
Visualization
Inference
Verification (data to spec) & Validation (data/spec to reality) for data quality

## Slide 16: Information is also an asset, having its own LC
Create information
Enrich data
Support decision making
Learn / innovate
CAD systems
GIS systems
Add semantics
Add links
e.g. Urban
Strategy
Information models
Analysis models
BIG
DATA
OPEN & LINKED
SMART INFO
1
2
3b
4
5
6
7
8
Analyse / simulate
Manage information
DERIVEDINFO
Monitor
Acquire (big) data
3a
BIM
GIS
Basis for Digital Twins!

## Slide 17: ALIM Gremia
Many organizations and topics involved

## Slide 18: Some selected highlights 2021, NL bias
ISO ICDD-1/2
NEN NTA 8035, https://www.nen.nl/nta-8035-2020-nl-266070
CEN TC442/WG4/TG3 Semantic Modelling and Linking (SML) - ENQ draft standard (prEN 17632:2021)
NEN 2660-1 (v. 0.7) & 2660-2 & WG “Praktische voorbeelden”
COINS&CB-NL Expertgroep Best Practices
Geonovum Meta Informatie Model 1.1 (MIM), https://docs.geostandaarden.nl/mim/wv-st-mim11-20191029/
NEN 3610-LD, https://geonovum.github.io/NEN3610-Linkeddata/
DIS Geo SOR, https://docs.geostandaarden.nl/disgeo/hiso/, https://docs.geostandaarden.nl/disgeo/emso/#sor-begrippen-objecttypen-en-typeringen
BZK Totaal Driedimensionaal (T3D) programma (VNG, Den Haag, Rotterdam, Amsterdam)
  https://github.com/MichelBohms/dataserver/blob/master/20201026%20Interbestuurlijke%20klankbordgroep%20T3D%20(incl%20verslag).pptx
IMBOR OTL, GWSW OTL. Amsterdam OTL
CB-NL taxonomie, NEN 2727 meronomie (for inspections)
digiGO
  Digitaal Stelsel Gebouwde Omgeving (DSGO), https://www.digigo.nu/dsgo/default.aspx
  versnellingsproject “NEN 2767 <> IMBOR harmonisatie” (a.h.v. NTA 8035/NEN2660)
bSI
  ifcOWL, https://standards.buildingsmart.org/IFC/DEV/IFC4_1/OWL/index.html
  BCF XML, https://github.com/buildingSMART/BCF-XML
  BCF REST API, https://github.com/buildingSMART/BCF-API
W3C LBD BOT Ontology, https://w3c-lbd-cg.github.io/bot/

## Slide 19: What’s hot
time
NTA 8035
Conceptual
Bindings for LD
Top Level Model
NEN 2660-1
NEN 2660-2
Conceptual configured
Top Level Model extended
Binding for LD
Dis Geo IMSOR
Geonovum
MIM 1.1
CEN TC442 SML Part 1 / Part 2
NEN 3610-LD
Conceptual
Top Level Model (generic)
T3D
Language conceptual
Top Level Model (generic)
CBNL / NEN2767 / IMBOR / GWSW
bSI (IFC+bSDD)
IfcOWL or JSON Route …
ISO 12006-3
BIM
OTL

## Slide 20: ALIM
Rijkswaterstaat
Provincie Gelderland
BIM Loket
Semmtech
Croonwolter&dros
TNO
Supported by:
With the sector NTa8035/NEN2660
Note: Some demand-side & Infra bias, but improving …

## Slide 21: ALIM images
Kadaster DIS Geo

## Slide 22: ALIM Images
Prorail

## Slide 23: ALIM
Example AT Provinces & municipalities: IAMPRO
Example: Rioned/GWSW using our NTA8035
NTA
top level
ontology
“on top”
NTA
language
“under the hood”

## Slide 24: 02 planning for ALIM
Basics
Perspectives
Core Data Models & Data Sets

## Slide 25: 02 Planning for ALIM
Define the use case, what is the purpose of ALIM?
  What business process is to be supported/improved?
    - Apply Business Process Model & Notation (BPMN) as technique
    - Life-cycle or supply-chain communication? (data exchange or data sharing scenario?)
  What stakeholders are involved?
  What software functionalities are involved? Existing (to integrate) or new (to develop)?
What kind of ALIM is required? Referred to as “Levels of Capability” in NTA 8035/NEN 2660/CEN SML:
  Data alignment for humans
  Data exchange/sharing
  Data integration & innovation
Basics

## Slide 26: 02 Planning for ALIM
Which views are relevant?
  Define an information architecture involving all relevant views/sources related to humans & software
Typically
  Life cycle phase: plan, design, build & operate (manage & use) views
  Supply chain stage (client, contractor, supplier views)
  Discipline View (related to aspect systems of asset: safety/structural integrity, energy efficiency, circularity, …)
  Technical. i.e.
    - Vocabulary/dictionary/thesaurus terms/definitions
    - Ontology classes
    - Ontology attributes & relations
    - Ontology constraints & rules (definitional)
    - Ontology constraints & rules (law & regulations)
    - Ontology constraints & rules (client brief)
    - Ontology constraints & rules (sector recommendations)
perspectives
Open World Assumption
(inference)
Versus
Closed World Assumption
(verification)

## Slide 27: 02 Planning for ALIM
Linked Data approach in most flexible form: all views are independent & linked
Practical: model overlap in separate core information models / information sets where possible
Different reuse layers, can be both information model or (reference) information set
  Worldwide EU Inspire network ontology, ifcOWL, W3C LBD BOT ontology, GeoSparql, ….
    W3C Time ontology, W3C/OGC GPS ontology (WGS84), …
  National NWB data set, CBNL, NEN2660, NTA 8035, DisGeo IMSOR, NEN 3610, …..
  Organization Amsterdam, CROW, Tennet OTL, Alliander, …
  Application RWS BMS DISK OTL
  Project ProRail Emmen-Zuid OTL
Core information model advantage: no mapping/conversion needed
Core information set advantage: single source of truth (SSoT)
One organization > one governance > one corporate core data model/set possible, extendable for various internal LC, discipline or technical views/perspectives
Core information Models & information sets

## Slide 28: planning for alim
Which relevant (orthogonal) dimensions?
Which relevant options per dimension?
Perspective = combinations of one option per dimension
#perspectives: #options d1 X #options d2 X #options d3 ….
Combining perspectives: intersections (“AND”) and unions (“OR”)
  Over some options per dimension?
  Over all options per dimension?
  Over multiple dimensions?
  Example: Upper like nen2660.ttl ontology: intersection over all options of all dimensions
perspectives

## Slide 29: planning for alim
3 Dimensions and their options
  Discipline (5 options)
    1. Verhardingen (Roads)
    2. Civiele infra (Civil structures, potentially split in fixed and movable)
    3. Bomen (Trees)
    4. Groen (Green)
    5. Verkeers Informatie Systeem (VIS) (Traffic Info System)
    6. Openbare Verlichting (OVL) (Public Lighting)
  Life-cycle phase (3 options)
    1. Systems Engineering (SE)
    2. Ingenieursbureau (IB) (Engineering)
    3. Verkeer & Openbare Ruimte (V&OR) (Asset Management)
  Technical (6 options)
    1. Classes (URIs only or already typed)
    2. Labels and definitions
    3. Datatypes & Enumeration Values
    4. Taxonomy (rdfs:subClassOf properties)
    5. Properties (RDF properties so datatype properties and object properties)
    6. Constraints (potentially split ontologically, i.e. by definition and for client brief, regulations etc., i.e. by usage)
    Total amount of 90 perspectives: 5 x 3 x 6
perspectives: Amsterdam example

## Slide 30: planning for alim
Intersection over all: nen2660-owl.ttl
Union over all life-cycle phase options to be able to talk about same thing over its life-cycle (“in time”)
Intersection over all discipline options to be able to connect the various aspects of an asset (“in view”)
Combining perspectives

## Slide 31: planning for alim
2 perspectives
X1
X1_1
Y1
Y1_1
X
Y
Perspective 1
Perspective 2
Class
Individual
type
Class
subClassOf
subClassOf
type

## Slide 32: planning for alim
Interrelating perspectives
X1
X1_1
Y1
Y1_1
sameAs
X
Y
equivalentClass
Perspective 1
Perspective 2
== two-way subClassOf
Class
Individual
type
Class
subClassOf
subClassOf
type

## Slide 33: planning for alim
Under one governance better decided!
X1
X1_1
Or
Y1_1
Y1
X
or
Y
Core instance in intersection
Core concept in Intersection
Class (specific)
Individual
type
Class (generic)
subClassOf
subClassOf
type

## Slide 34: 03. defining for ALIM
Specification types
Fundamentals
Top Level Model
Technology
Ontology
Example (from NEN/TNO/RHDHV NTA8035 workshops)

## Slide 35: 03. defining for ALIM
Vocabulary
  Terms
Dictionary
  + Definitions
Thesaurus
  +weak hierarchy (higher/lower)
Ontology
  Concepts, Attributes, Relations
  Constraints, Derivations
  Taxonomy – subClassOf, specialisation
  Meronomy – typical hasPart, typical decomposition (“breakdown structure” )
Specification types

## Slide 36: 03. defining for ALIM
Specification types, related view
LinkedIn, Dr Nicolas Figay

## Slide 37: 03. defining for ALIM
Four abstraction mechanisms
  Thing <> Symbol describes (the Meaning Triangle)
  Classification (inverse: Instantiation) type ↑ > Typology
  Generalization (inverse: Specialization) subClassOf ↑ > Taxonomy
  Composition (inverse: Decomposition) hasPart ↓ > Decomposition/Meronomy
Not in the same league! (not “orthogonal”)
First: Classification, resulting in a Typology
Fundamentals

## Slide 38: defining for ALIM
Some Fundamentals: the meaning triangle
Consciousness
Reality
Language

## Slide 39: defining for ALIM
Some Fundamentals: must read …

## Slide 40: defining for ALIM
Some Fundamentals: the meaning triangle
“nl:Bridge_123”
symbolises
conceptualises
represents
Thought
Thing
Symbol
Synonyms
Referent
Object
Phenomenon
Synonyms
Reference
Concept
Idea
Synonyms
Sign
Representation
Physical
Object
“
“

## Slide 41: defining for ALIM
Some Fundamentals: the meaning triangle
Recursive application
Thought
Thing
Symbol
Language-dimension
Thought
about
symbol
Symbol
for
symbol
Symbol
seen as
Thing
Often “behind the language” like:
OWL in RDFS
Extended Backus-Naur Form (EBNF)
Closures via self-reference like
  EBNF in EBNF … or
  SHACL in SHACL

## Slide 42: defining for ALIM
Knowledge Model
Information Model (like Ontology)
Information Set
2 roles of an information model
Information Model as model of
an information set (“active”)
Knowledge as instance of
the Knowledge Model
(“ passive” )

## Slide 43: defining for ALIM
Comparison DNA

## Slide 44: defining for ALIM
Typology, typical focus for knowledge modelling
Information Model
(like Ontology)
Lexus (the brand)
Knowledge Model
classification
or “type”
CarManufacturer

## Slide 45: defining ALIM
Typology, typical focus for information modelling
Information Model
(like Ontology)
Information Set
Classification
or “type”
Lexus (the brand)
MyLexus

## Slide 46: defining ALIM
Some Fundamentals: the meaning triangle
Thought
Thing
Symbol
Language for KM
Language for IM
Language for IS

## Slide 47: Defining alim
Information Set
Information Model (like Ontology, Schema, Diagram, …)
Meta-information on Information Set & Information Model
Meta-information level options for 3.
  Whole
    - whole information set, whole information model
    - Example: this information set is defined by Kadaster
  Part
    - per concept, relation, attribute or object, relation reference, attribute value
    - Example: certain tree height value having a precision 0.1
  Language atom
    - like triple, think RDF reification
  - Example: “:MyTree rdf:type Tree” is 90% true or “:Tree rdfs:type rdfs:Class” is stated by Michel
areas for information modelling

## Slide 48: 03. defining for ALIM
Fundamentals, typology
Knowledge Model
Information Model
(like Ontology)
Information Set
classification
or “type”
classification
or “type”
CarManufacturer
Lexus (the brand)
MyLexus

## Slide 49: 03. defining for ALIM
Fundamentals, taxonomy
Information Model
(like Ontology)
Information Set
GS450h (model)
MyLexus
Car
Lexus (brand)
generalisation
or “subClassOf”
classification
or “type”

## Slide 50: 03. defining for ALIM
Fundamentals, Meronomy
Information Set
Information Model
Battery
Chassis
Engine
decomposition
or “hasPart”
classification
or “type”
Radiator
Lexus
Wheels
MyBattery
MyChassis
MyEngine
MyRadiator
MyLexus
MyWheels
X
Y
Z
constraint
or typicalHasPart (derived)
X
constraint (restriction/shape)
for hasPart
exactly 1 Y
min 1 Z

## Slide 51: 03. defining for ALIM
Top Level model, concepts
TopConcept (the “root”)
  ConcreteConcept
    Entity
      Object
        PhysicalObject
        InformationObject
      Activity
    State
    Event
  AbstractConcept
    GeometricEntity
    TemporalEntity
    Type
      EnumerationType
        Unit
        QuantityKind
      ObjectType
    Objectification
      QuantityValue
      QualityValue
      RelationReference

## Slide 52: 03. Defining for alim
Top level model, relations/attributes
van | relatie/attribuut | naar
TopConcept | isDescribedBy | InformationObject
Entity | hasState | State
Entity | triggers | Event
PhysicalObject | performs | Activity
ConcreteConcept | hasTemporalEntity | TemporalEntity
ConcreteConcept | hasInterior | GeometricEntity
ConcreteConcept | hasBoundary | GeometricEntity
Activity | transforms | Object
Event | begins | State
Event | ends | State
ConcreteConcept | hasPart | ConcreteConcept
TopConcept | abbreviation | String

## Slide 53: 03. defining for ALIM
Top level model, More dimensions
Real
Object
Technical
Entity
Functional
Entity
Spatial
Region
“ALIM”
Realized
Entity
Planned
Entity
Physical
Object/
Entity
“ACREAGE”
“ALIM dimensions”
  ~Systems Engineering (SE) dimensions
All Optional
All Disjunct

## Slide 54: 03. defining for ALIM
Q1 | Q4
Q2 | Q3
FunctionalEntity
TechnicalEntity
PlannedEntity
RealizedEntity
isImplementedBy
isRealizedBy
Planned functional
spatial region
Geplanned functional
real object
Planned technical
spatial region
Planned technical
real object
contains
Realized technical
spatial region
Realized technical
real object
contains
Realized functional
spatial region
Realized functional
real object
Q1a
Q1b
Q4a
Q4b
Q2a
Q2b
Q3a
Q3b
check
isBoundBy
isBoundBy
check
check
check
contains
contains
isBoundByObject
isBoundByObject

## Slide 55: 03. defining for ALIM
Graphically
ALIM
Design
object
Build object
Operate
object
Program space
Program
object
Operate
space

## Slide 56: 03. defining for ALIM
Top level model, More patterns
Topology, Connections, Ports, Interfaces (for networks…)
Geometry (BIM/GIS common issue)
Time (W3C Time Ontology)
Matter
  Pure chemical substances (elements/bondings)
  Mixtures (homogeneous/heterogeneous)
  Portions
Implicit Groups

## Slide 57: 03. defining for ALIM
Technology facets
  Formats for information sets and information models
  Direct access mechanisms (APIs, Query Languages)
  Identification schemes like URI-strategies
Alternative “solutions”
  Microsoft Excel (tabular/CSV data)……………open? semantic enough?
  ISO STEP (SPFF, EXPRESS), primary tech for bSI IFC
  OMG MDA (UML, MOF, XMI)
  W3C XML (XML, XSD, Xpath, XQuery, …)
  From standard (micro) web services development: REST-based Open APIs, JSON/JSON Schema, GraphQL
  100 exotics …
  W3C Linked Data / Semantic Web technology
Technology, many options

## Slide 58: 03. Defining for alim
Technology, W3C Linked Data / semantic web
Passive Role (KM)
Active Role
R – Reusable
I - Interoperable
A - Accessible
F – Findable

## Slide 59: 03. defining for ALIM
100% based on Internet/WWW, the base communication infrastructure
Most powerful modelling language (think constraint modelling)
Well-defined in logic, maths and graph theory
Based on a "Triple" as data atom, only create or delete, no change; merging becomes adding
Fully generic solution, domain-independent
Software tools available for all ALIM LC phases
Most suited for distributed solutions and interlinking
Technology, W3C linked data/semantic web, advantages

## Slide 60: Defining alim
The Triple as data atom: <Subject Predicate Object>
Sets of triples form graphs
S, P, O: all three web addresses (Object can also be a value)
In general:
Example:
RDF – Resource Description Framework
<https://w3id.org/def/voorbeeld/Brug>
rdfs:label
“Bridge”@en
Subject
predicate
Object

## Slide 61: Defining alim
RDF example
subject
object
predicate
IJsselbridge
(123.3,-6.2)
hasLocation
TrafficBridge
2DCoordinates
type
type
Infra asset
subClassOf
Location
subClassOf
url
url
url
url
url
url
Semantic Web
FOCUS
Linked
Data

## Slide 62: Defining alim
LD versus relational
Relational view
Subject | attr1 | attr2 | rel1
Subject_1 | a | b | Subject_2
Table X
Semantic view
Subject | Predicate | Object
Subject_1 | rdf:type | X
Subject_1 | attr1 | a
Subject_1 | attr2 | b
Subject_1 | rel1 | Subject_2

## Slide 63: Defining alim
  RDF/XML / TriX
  TURTLE / TriG
  N-TRIPLE
  JSON-LD
All equivalent, Turtle best for modeller, JSON-LD for implementer
RDF Formats

## Slide 64: Defining alim
SKOS (itself in RDFS+OWL)
RDF (triple+rdf:type)
RDFS (RDF Schema)
RDFS+OWL – Web Ontology Language
RDFS+SHACL
Note: OWL (and SHACL) is a layer on top of RDFS
RDF languages

## Slide 65: Defining alim
RDF* (“RDF Star”)
Turtle*
SPARQL*
“RDF Reification logically treated”
  Enabling statements about statements
https://w3c.github.io/rdf-star/, RDF-star and SPARQL-star, Draft Community Group Report 13 February 2021
RDF languages future

## Slide 66: 03. Defining for alim
Concepts
(Reference) Individuals
Value types
Attributes
Relations
  Instantiation
  Specialisation
  Grouping
  Association (incl. decomposition)
Constraints & Derivations
Groups
height
weight
price
Ontology, what is in?

## Slide 67: 03. Defining for alim
Ontology, what is in?

## Slide 68: 03. Defining for alim
OWL is (by default) “Open World”:
Everyone can say anything about anything
If no explicit constraint is defined, then every attribute and relation is in principle relevant to every concept.
Therefore attributes / relations are defined separately from concepts
SHACL is (by default) “Closed World”
Ontology, Open world assumption (OWA)

## Slide 69: 03. Defining for alim
Example schematic
Bridge
BridgeDeck
ConcreteSlab
Vehicle
height
compliesToSpeedLimit
weight
vehicleSpeed
NonGeometricVehicleAttributes
{ … }
accuracy

## Slide 70: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
example ontology/OTL

## Slide 71: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model concepts

## Slide 72: 03. Defining for alim
:Bridge
a owl:Class ;
rdfs:label "Bridge"@en ;
rdfs:label "Brug"@nl ;
rdfs:subClassOf nen2660:PhysicalObject ;
skos:definition “Connection for traffic between two abutments that is separated by water."@nl .
Note the various annotations.
Example, OWL code

## Slide 73: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model simple qualities

## Slide 74: 03. Defining for alim
:compliesToSpeedLimit
a owl:DatatypeProperty ;
rdfs:domain :Vehicle ;
rdfs:range xsd:boolean .
Example, OWL code for simple (Boolean) quality

## Slide 75: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model enumeration qualities

## Slide 76: 03. Defining for alim
:weight
a owl:ObjectProperty ;
rdfs:domain :Vehicle ;
rdfs:range :WeightType .
:WeightType
a owl:Class ;
rdfs:subClassOf bs:EnumerationType ;
owl:oneOf (
:Light
:Medium
:Heavy ) .
:Light
a :WeightType .
:Medium
a :WeightType .
:Heavy
a :WeightType .
Example, OWL code for enumeration type

## Slide 77: 03. Defining alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model quantities

## Slide 78: 03. Defining for alim
:height
a owl:ObjectProperty ;
rdfs:range bs:QuantityValue ;
nen2660:quantityKind quantitykind:Length .
:vehicleSpeed
a owl:ObjectProperty ;
rdfs:domain :Vehicle ;
rdfs:range bs:QuantityValue ;
nen2660:quantityKind quantitykind:Speed .
:accuracy
a owl:ObjectProperty ;
rdfs:range bs:QuantityValue ;
.
Example, OWL code for quantities
This is a meta-quantity for a quantity!

## Slide 79: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model relations

## Slide 80: 03. Defining for alim
:hasVehicles
a owl:ObjectProperty ;
rdfs:domain :Bridge ;
rdfs:range :Vehicle .
Example, OWL code for a relation

## Slide 81: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model restrictions

## Slide 82: Defining for alim
:Bridge
…
rdfs:subClassOf [
a owl:Restriction ;
owl:cardinality "1"^^xsd:nonNegativeInteger ;
owl:onProperty :height ;
] ;
rdfs:subClassOf [
a owl:Restriction ;
owl:onClass :BridgeDeck ;
owl:onProperty nen2660:hasPart ;
owl:qualifiedCardinality "1"^^xsd:nonNegativeInteger ;
] .
Example, OWL code for restrictions

## Slide 83: 03. Defining for alim
Bridges always have exactly one height expressed in meters. Bridges always consist of exactly one bridge deck that itself consists of one or more concrete slabs. At a given moment there are 0 or more vehicles on a bridge with a certain speed measured in kilometers per hour (with an accuracy of 90%) and of a certain weight class that can only be selected from light, medium or heavy. It is known for each vehicle whether they are complying with the applicable speed limit at that time. Weight class and speed are grouped as non-geometric vehicle properties.
Example, Identify & model groups

## Slide 84: 03. Defining for alim
:NonGeometricVehicleAttributes
a rdfs:Container ;
rdfs:member :weight ;
rdfs:member :vehicleSpeed ;
rdfs:member :compliesToSpeedLimit .
Example, OWL code for a group

## Slide 85: 03. Defining for alim
:Bridge_1
a :Bridge ;
nen2660:hasPart :BridgeDeck_1 ;
:hasVehicles :Vehicle_1 ;
:height [
rdf:value 50.0 ;
nen2660:unit unit:M ;
] .
:BridgeDeck_1
a :BridgeDeck ;
nen2660:hasPart :ConcreteSlab_1 ;
nen2660:hasPart :ConcreteSlab_2 ;
nen2660:hasPart :ConcreteSlab_3 .
Example, instances
:Vehicle_1
a :Vehicle ;
:weight :Heavy ;
:compliesToSpeedLimit true ;
:vehicleSpeed [
rdf:value 128.0 ;
nen2660:unit unit:KiloM-PER-HR ;
:accuracy [
rdf:value 0.9 ;
] ;
] .

## Slide 86: 04. implementing ALIM in software
Overview
Integrated Development Environment (IDE)
Common Data Environment (CDE)
Integrating existing software applications
Application Services (“cloud native”)

## Slide 87: 04. implementing ALIM in software
Integrated Development Environment (IDE)
  Used for ontology & mapping development
Common Data Environment (CDE)
  Data Storage & Access
    - RDF Triple Stores
    SPARQL query language (GraphQL as possible frontend)
    - Other Graph databases (like Property Graphs: Neo4j)
    Cypher query language (GraphQL in the labs)
  Transformer Tools
    - Mappers (between data models)
    - Translators (data set format)
    - Convertors (data set meaning)
overview

## Slide 88: 04. implementing ALIM in software
TopQuadrant TopBraid Composer (TBC) RDF/RDFS/OWL/SHACL-editor
Stanford Protégé/Web Protégé (open source) OWL-editor
Semmtech Laces
WeaverHQ
Cognitum Fluent Editor
...many
Integrated development tools (IDE), examples

## Slide 89: 04. implementing ALIM in software
IDE Example: TopBraid Composer (TBC) ME version 7.0.3

## Slide 90: 04. implementing ALIM in software
CDE
©PCSG/BIM Today 2016

## Slide 91: 04. implementing ALIM in software
Example CDE for linked data: GraphDB

## Slide 92: 04. implementing ALIM in software
Integrating existing applications
Translator
native
XML
SPFF
…
Turtle
RDF-XM:
JSON-LD
Translator
SPARQL
Some API
File-
based
Direct Access
-based

## Slide 93: 04. implementing ALIM in software
Integrating existing applications
Translator
native
XML
SPFF
…
Turtle
RDF-XML
JSON-LD
Ap-specific
Ontology

## Slide 94: 04. implementing ALIM in software
Integrating existing applications
information exchange
Translator
Ap-specific
Ontology
Translator
Ap-specific
Ontology
Covertor
Typically in the supply chain (involving change of ownership)
* Direct or via a
“Linking Rule Set”
By reference
like
equivalentClass/Property*

## Slide 95: 04. implementing ALIM in software
Integrating existing applications
information sharing
Translator
Ap-specific
Ontology
Translator
Ap-specific
Ontology
By reference
like
sameAs*
Typically in the life cycle (having multiple “single sources of truth”)
* Direct or via a
“Linking Data Set”

## Slide 96: 04. implementing ALIM in software
Open API (former Swagger): JSON/YAML defined, REST-based
GraphQL
Container Orchestration/Workflows (Kubernites)
Containerisation (Docker)
  Providing programming language/platform independence
  Like virtualisation did for the hardware
Map & Reduce distribution
Relationships with Linked Data
  GraphQL-LD
  JSON-LD
  Graph storage backends like MongoDB
    - involving BSON: Binairy JSON
Application services

## Slide 97: 04. implementing ALIM in software
Eaxmple Kadaster

## Slide 98: 05. Using ALIM in practice
Overview
Example TNO ERP-SI application
Example Digital Twins

## Slide 99: 05. Using ALIM in practice
ALIM for information exchange, information sharing & information integration
  Start simple: information exchange scenario
  One step up: information sharing scenario (single source of truth, compare “BIM Level 3”)
  Finally, data integration involving a new functionalities/services provided
More complex scenario’s: ALIM as kernel for Predictive Digital Twins
We start with a TNO example for data integration
  TNO ERP-SI, Early Research Program-Structural Integrity (ERP-SI) 2020
  Steel bridges, SI evaluation
  AI (Bayesian probability) applied to FEM parameters
Overview

## Slide 100: 05. Using ALIM in practice
ERP-SI, starting principle
Quickscan
OK
Unsure
Critical
Expert judgement with Digital Twin
Full FEM
Minimal Effort
80% result, 20% effort
Large effort (multi year, multi-FTE)
Relative classification of structural integrity
Absolute approximation of structural integrity
Engineering judgement on most critical points
Fast approximation of structural integrity
Easily repeatable with new data and insights
Limited amount of sensor data
Relatively ‘simple’ analysis models
Absolute classification of structural integrity
(sheet by Arpad Rozsas)

## Slide 101: 05. Using ALIM in practice
ERP-SI, Total process
6.
Probablistic
Analysis
4.
AS-IS FEM
Analysis
3.
Prepare
AS-IS FEM
9.
TO-BE FEM
Analysis
2.
Specify
Anomalies
1.
Specify
Bridge
5. / 12.
Measure
Bridge
7.
Define
Measures
10.
Analyse
& Decide
Measure
11.
Implement
Measure
13.
Validate
?
8.
Prepare
T0-BE FEM
sensors
realization
prior
posterior
? ProbAnal. == 3.

## Slide 102: 05. Using ALIM in practice
Erp-si, ideal AS-IS part
Bridge Ontology
(incl. geometry)
AS-IS Bridge
data & docs
Anomaly
Ontology
AS-IS Bridge
anomalies
data & docs
FEM
Ontology
AS-IS FEM
6.
Probablistic
Analysis
(ProbTaralli)
NTA-8035/NE-2660/CEN-SML
Measurement
Ontology
Measurement
data
4.
AS-IS FEM
Analysis
(ABAQUS)
3.
Prepare
FEM
FEM Results
Ontology
AS-IS FEM results
1.
Specify
Bridge
2.
Specify
Anomalies
5.
Measure
Bridge
(sensors)
prior
posterior

## Slide 103: 05. Using ALIM in practice
ERP-SI
bridge:residualLifespan
rdf:type owl:ObjectProperty ;
rdfs:range sml:QuantityValue ;
sml:quantityKind quantitykind:Time ;
sml:unit unit:YR ;
.
Taxonomy
Meronomy
Property
Bridge Ontology

## Slide 104: 05. Using ALIM in practice
ERP-SI
Taxonomy
Property
anomaly:rotationalStiffness
rdf:type owl:ObjectProperty ;
rdfs:domain anomaly:PartialLockingRotation ;
rdfs:range prob:StochasticValue ;
sml:quantityKind anomaly:RotationalStiffness ;
sml:unit anomaly:N-M-PER-RAD ;
.
Property detail
Anomaly Ontology

## Slide 105: 05. Using ALIM in practice
ERP-SI
aib:PartialLockingRotation_1
rdf:type anomaly:PartialLockingRotation ;
anomaly:forPhysicalObject ib:Pillar_F ;
anomaly:globalEffect false ;
anomaly:parameterType anomaly:Deterministic ;
anomaly:rotationalStiffness [
prob:posteriorMean [
rdf:value "2500"^^xsd:float ;
] ;
prob:posteriorStdev [
rdf:value "1100"^^xsd:float ;
] ;
prob:priorDistributionType prob:UniformDistribution ;
prob:priorMean [
rdf:value "5.0E14"^^xsd:float ;
] ;
prob:priorStdev [
rdf:value "2.89E14"^^xsd:float ;
] ;
] ;
.
Actual Data Set

## Slide 106: 05. Using ALIM in practice
ERP-SI
Simple Query:
“Give me all identified anomalies, the bridge part effected en whether they have a global effect or not”
PREFIX anomaly: <https://w3id.org/def/anomaly#>
PREFIX rdf: <http://www.w3.org/1999/02/22-rdf-syntax-ns#>
SELECT *
WHERE {
?Anomaly rdf:type/rdfs:subClassOf* anomaly:Anomaly .
?Anomaly anomaly:forPhysicalObject ?BridgePart .
?Anomaly anomaly:globalEffect ?GlobalEffect
}

## Slide 107: 05. Using ALIM in practice
TNO Vision 2021
Digital twins

## Slide 108: 05. Using ALIM in practice
Capabilities of Digital Twins
Digital twins
© Norwegian University of Science and Technology

## Slide 109: 05. Using ALIM in practice
Digital twins, data LC
Control
&
Learn
Analyse
Compare &
Decide
ALIM: Data Sets & Data Models
Create
Data Services
(store, visualize, clean, transform)
Control
Learn
Assets in reality (field or lab; real or scaled):
buildings, roads, bridges, tunnels, …
Capture
Common
Data Environment
(CDE)
Sensors
Actuators
manual or connected/streaming

## Slide 110: 05. Using ALIM in practice
Digital twins
architecture
Digital Twin System
High Level Architecture
Sensors
Asset layer
Communication layer
Data layer 1
Raw Data
Processed
Data
Meta Data
Other Data
Sources
Documents
BIM Data
Sensors
Sensors
Data layer 2
Data layer 3
Data Broker
Semantic Data
Ontologies
Digital Twins
Framework
Visualisation of Data
AI
Models
Data Pre-processing
FEM Models
Visualisation of DT
Data Analytics
Processing layer
Visualisation layer
Platform
Management
AAA
DT
Orchestration
Data
Management
Registry
Monitoring & Logging

## Slide 111: 06. Very Quick guide
Define a process model for your ALIM context & scope
Identify the relevant information flows, information perspectives ( “views”) and software applications
Define ontologies for the various information flows/perspectives
  Choose linked information language and linked data format
  Check for core information model / information set potential
  Integrate documents via meta-information and linking (hybrid approach)
  Define ontologies making as much as possible use op the SML top level (core) model
  Interlink them in a network
Exchange or share information & Integrate information by linking
Exploit integrated information like via new functionalities like digital twins

## Slide 112: Sheet pool

## Slide 113
Worldwide
  ISO
  W3C
  OMG
In Europe
In The Netherlands
  NEN
    - 2660 part 1 & 2660 part 2
    - CBNL
    - VISI
    - COINS 3.0 Best Practices
    - Geonovum/Kadaster/Gemeenten Meta Informatie Model (MIM)
  BIM Loket
  digiGo Digitaal Stelsel Gebouwde Omgeving (DSGO), https://digigo.nu

## Slide 114: Application area
Assets in the Built Environment:
  Buildings, civil and energy Infrastructures and Maritime Constructions
  Their aggregates (road/rail networks, building portfolios, airports, harbours, cities, …) and their parts (systems, elements, components & building materials)
  Assets can be Products: “assets you can buy”
Asset Life-cycle Management (== project management + use/asset management) covering phases:
  Program
    Initiate new or maintain (“rebuild”), renovate (“re-design+re-build”), re-purpose (“re-program+re-design+re-build”)
    Ultimate re-purpose (“no more purpose”): Demolish, recycle & reuse
  Design & Build
  Operate
    Use & Manage use; input to Programming
    Manage asset: Assess condition and performance of asset; input to Programming
    Asset Supply-chain (relevant for each LC phase) covering demand and supply stages:
  Client (public, commercial), Contractor, Sub-contractor, Supplier, Manufacturer
  Typically following the asset breakdown structure in parts

## Slide 115: digitalisation
Data & Software
All actors in the life-cycle and supply-chain of an asset have to
  Manage asset data
  Exchange or share asset data
  Use the data for better decision making
  Use software manipulating the data in all above
Therefore, the right, future-proof Modelling of Assets is crucial!
Following the whole data life-cycle:
  Data Acquisition (manual, monitoring, 3D scanning, …)
  Data Analysis, Calculation, Simulation
  Decision Making and implementing based on the data
  Learning from the data

## Slide 116: asset lifecycle information modelling (ALIM)
The modelling of information of an Asset in the built environment in or over its lifecycle and supply-chain, covering:
Various types of data (in practice always a hybrid situation)
  Unstructured
  Structured data (machine-processable)
    Syntax (format, serialisation)
    Direct Data Access (query languages, APIs)
  Semantic data (machine-interpretable)
    Semantics (meaning, structure) defined explicitly in diagram, schema, ontology, etc.
All in documents/files, sometimes packaged/zipped in containers
Exchanged (copied, mailed, …) or Shared (like on a web site in the cloud)

## Slide 117: asset lifecycle information modelling (ALIM)
          ALIM is covering and modelling/linking all data typically related to
            Systems Engineering (SE) : - as-required
            Building Information Modelling (BIM) - as-designed, as-built, (as-operated); static
            Geo-spatial Information System (GIS) - (as-built), as-operated; static
            Monitoring & Control (M&C) - as-operated; dynamic; connection to reality
            Document Management (DM) - all

## Slide 118: asset lifecycle information modelling (ALIM)
ALIM
BIM
SE –
Systems
Engineering
GIS
M&C –
Monitoring &
Control
operate & program
design
build& operate
operate
operate
operate

## Slide 119: ALIM
Life-cycle & Supply-chain
Software
Real Asset
  Incl. inspections, sensors & actuators
ALIM powered by Linked Data
  Modelling & Linking
  Data & documents
Software
  Common Data Environment (CDE)
  CAD, FEM, ERP
  AI/ML
  Beheer/Onderhoud Management Systemen (BMS/OMS)
Asset Life-cycle (PDBO)
Asset Supply-chain
  Client, Contractor, Supplier/Manufacturer
Digital Twin
BIM
GIS
Systems
Enginering
Operate
Program
Build
Design
Project Management
Asset Management
Software
Inspection/
Monitoring
Data

## Slide 120: ALIM LC phases (as asset LC metaphore)
Program ALIM > Why do we need ALIM?
Design ALIM > What does the ALIM look like conceptually ?
Build ALIM > How to Implement ALIM in Software?
Operate ALIM > Use of ALIM in Practice
Many detailed steps per phase

## Slide 121: Steps per phase: program alim
Program > Why do we need ALIM?
  Context
    Determine asset (sub)type
    Determine lifeccyle phase and supply-chain stage relevance
  Select Use Case type
    Alignment of Terminology and Definitions
    Data exchange/sharing with partners (involving IERs)
    Data integration for decision support (specific roles for data linking & data validation/verification)
    ALIM as fundament for a standard/semantic Digital Twin: adding software functionalities and two-way connection with reality with sensors actuators
  Identify relevant software application landscape (BMS, OMS, …)
  Identify nature of data situation: AS-IS and TO-BE (growth path):
    from documents via structured data to semantic data, and
    from proprietory to standard data

## Slide 122: Steps per phase: design alim /1
Design > What does the ALIM look like?
  Accept Design Principles
    Findable, Accessible, Interoperable, Reusable (FAIR), Standard, Semantic, Simple, Scalable, Separation of Concerns (SoC), Single Source of Facts (SSoF), Multiple Sources of Truth (MSoT)
  Use standard Modelling and Linking approaches (NTA 8035/CEN SMLS: in NL: COINS 3.0 Best Practices) all based on W3C Linked Data technology (“Linked Data –Powered”)
  Choose Level of Capability (LoC) needed (SKOS, RDFS, OWL, SHACL)
  Choose serialisation (RDF/XML, Turtle, JSON-LD) and/or Direct Data Access method (like SPARQL, GraphQL-LD or related APIs)
  Determine role of software appication data needs: the level of independence of software:
    Syntax-independent
    Semantics-independent

## Slide 123: Steps per phase: design alim /2
Design > What does the ALIM look like?
  Identify relevant networks of Data Sets and Ontologies and related/linked document (types)
  Identify reusable semantic resources (international/national standards): ontologies and reference data sets
  Select semantic Integrated Development Environment (IDE)
  Specify all ontologies and reference data sets following NTA/SMLS
  TBD: role of Application Ontologies
  Link ontology/dataset ‘modules’ together (by defining “Linking Rules/Data Sets” and/or Queries/APIs)

## Slide 124: Steps per phase: build alim
Build > How to Implement ALIM in Software?
  Choose Semantic Data Platform
  Choose Document Platform
  Implement ontologies, data sets, linking rule/data sets adn queries/APIs
  Connect end-user software (BMS, OMS, …) using
    Translators (for syntax) and/or Convertors (for semantics) or
    Queries/APIs

## Slide 125: Steps per phase: operate ALIM
Operate > Use of ALIM in Practice
  Proof of Concept (PoC) or for real

## Slide 126: Application of ALIM approach
Use case asphalt data analysis – KIP 2019 + KIP 2020
ERP Digital Twin – Structural Integrity – Steel bridge
Use case geographical linked data for infra, RWS and VU
Possibly other cases in KIP ALIM 2020
Maybe also other Digital Twins
At TNO Also outside TNO
OTL IMBOR Provinces
OTL IMBOR Amsterdam
BIM TenneT
AIRBIM RWS
Rioned GWSW
Kadaster – PDOK – BAG
Boskalis (+) - PIM

## Slide 127: For example use case smart asphalt data (2)
  Programming
  Analyse data requirements for asphalt data analysis with AI Note: data analysts did process analysis with domain expert => info requests they need!
  Analyse available data (
  Design
  Design ontology network + roadmap
  Build
  Develop ontologies
  Develop linking rule sets between ontologies
  Develop queries for data analysts
  Convert data to smart data etc.
  Operate
  Apply queries to the data
First focus = make data interoperable and reusable (--IR)

## Slide 128: ALIM standardization
NEN NTA 8035 Generic Modelling & Linking Patterns > CEN TC442 SMLS
Geonovum/Cadastre Meta Information Model (MIM)-LD
NEN 2660 Built environment-specific Modelling Patterns
BGT-OTL Ontology for GIS
BOR-OTL Ontology for Public Spaces (common for Cities/Provinces like Amsterdan, Gelderland etc.)
Rioned GWSW
CB-NL Built environment-specific Taxonomy
NEN 2767-4 Inspection Meronomy (typical class-level decomposition)
NLCS OTL
EU
  Inspire Road Network OTL
  CEN TC442 Semantic Modelling & Linking Standard (SMLS)
bSI ifcOWL, BOT, bSDD
ISO 19650 Project/Asset Management basics
ISO 21597 (ICDD) Containers with linked documents (semantic or not), ie meta-level packaging & transport
W3C Linked Data technology

## Slide 129: ALIM standardization related to phase
Core Ontologies
Systems Engineering (SE)
(functional requirements & technical boundary conditions) Ontologies
Project/BIM ontologies
Acreage/GIS ontologies
Monitoring & Control (M&C)
Ontology
Business (KPIs, costs, benefits) Ontologies
ifcOWL, BOT, NLCS-OTL,
NL-SfB-OTL
(as SHACL shapes)
NEN 2767-4
BGT-OTL, BOR-OTL, GWSW
OTL-Adam, OTL-NH, OTL-GL,
Aquo, …

## Slide 130: Typical IT architecture
Information sources
Computer applications & Services
Data lake
(Findable + Accessible)
Smart information
(Interoperable + Reusable)
OTLs
Meta data
Graphical user-interface
Asset Lifecycle Information Management (ALIM)
End user
Data Manager/Analyst
links
links

## Slide 131: For example use case smart asphalt data
AI applications
Smart asphalt data + asphalt OTLs
Tagged asphalt data files + unified database
Raw asphalt data

## Slide 132: Database compilation from existing TNO sources
A unified database from multiple sources:
  phase angle Excel sheet;
  shear modulus Excel sheet;
  data from multiple reports, e.g. sieve passing, temperatures (outside, hopper, beam), etc;
  raveling data from excel sheet.
~900 rows, 39 columns (= 39 different characteristics/parameters).
Many missing data points.
99% complete (Question: year/age).
Seems to be very uncertain, i.e. large measurement uncertainty (subjective, inspector dependent).

## Slide 133: Conclusions Data and predicting raveling
  With the currently available ravelling data predicting asphalt ravelling is practically impossible (with any reasonable accuracy and uncertainty). This is due to:
    poor data quality, e.g. sometimes the asphalt apparently self-rejuvenate, large variation between inspectors.
    crucial information is missing (e.g. if there was a maintenance, measurements from surfaces older than 8 years).
    the dataset is very small considering that there is virtually no first principle based theory to describe any aspects of asphalt ravelling (physics-based theories are lacking).

## Slide 134: STEP 1: Focus on pre-integrated unified data
property
unit
datatype
Actual data points

## Slide 135: STEP 3: adding semantics overview
Data sources
Zebravakken
data
DSR Test
data
Ravelling
data
Data lake
unified_ageing_asphalt_database.xlsx
Data conforming to semantics
unified_ageing_asphalt_database_DATA.ttl
Enriched*
“spreadsheets.owl”
Manually
Import
SPARQL Select Queries
* Compliant with
NEN NTA 8035

## Slide 136: Step 4: New data access functionality /1
“Give me all property definitions having a unit defined”
  SELECT DISTINCT ?propertydef ?unit WHERE {
  ?property a bsc:Property .
  ?property bsc:hasPropertyDef ?propertydef .
  ?propertydef bs:unit ?unit .
  }
  Giving:

## Slide 137: Dot on the Horizon
Importing the separate data sources in the data lake (flexible Step 1)
  Functionality needed to flexibly browse, select and combine data models / data sets
  Functionality needed to interlink them
All Described (by meta-data) and Modelled & Linked together in space and time in linked data ways involving as much as possible standard ways & ontologies like:
  NEN NTA/CEN SMLS generics
  Inspire DS Transport (Road) Network or OpenTNF ontologies
  Road Ontology ifc4OWL/RWS-OTL
  PIM Material ontology
  NEN 2767 / LCMS inspection data
  Sensor Measurement ontology like W3C SSN/SOSA
Using Linking Rule sets (asserted, generated or implicit in querying)
End-user scenario driven selection/configuration supporting specific data analyses
Planned for in the upcoming “KIP 2020 Proof of Concept Wegen” !

## Slide 138
ALIM
CDE / DBE*
Digital Twin (DT)
Linked Data
Software
“powered by”
M&C system
(sensors/actuators)
* CDE in Built Environment:
Digital Built Environment

## Slide 140
Digital Twin
Data Management
CDE / DBE, BIMServer, Semantische Servers. …
Data: ALIM (powered by LD)
SE, BIM, GIS, M&C (incl. Document Management) …
Meetsysteem
(sensoren & actuatoren)
Software Functionaliteiten
AI, BIM Bots, Beheer Management Systemen, …

## Slide 141: Trend Matrix towards DT
©Federico Cappuzzo,
Siemens Digital Industries Software,
2021 (on LinkedIn)

## Slide 142: Gemeentewerken Amsterdam

## Slide 143: Key Semantic resources
W3C/OGC Semantic Sensor Networks (SSN), https://www.w3.org/TR/vocab-ssn/
  Implementation of ISO 19156:2011, Geographic information — Observations and measurements
  Sensor, Observation, Sample, and Actuator (SOSA), a lightweight core of SSN
W3C Prov ontology
W3C Time ontology
W3C World Geodetic System 1984 (WGS 84) ontology implementing GPS coordinate system
  https://www.w3.org/2003/01/geo/wgs84_pos
  lat, long, alt & event (time stamp)

## Slide 144: Knowledge modelling
Classes can be seen as instances of meta-classes (in a Meta-Ontology or Knowledge Model)
Technically known as “OWL Punning”
Multiple rdf:type application in one line
Handy for modelling many subclasses (like product library items)
  Mapping the constraints to properties
Example: “Product” having 3 independent properties: x, y and z

## Slide 145: Thank you for
Your time