## Slide 1: CEN prEN 17632: Semantic Modelling and Linking (SML)
in the Built Environment | Michel Böhms, presented in ISO TC67 AG1

## Slide 2: overview
CEN preen 17632: Semantic Modelling and Linking (SML)
The playing field
01.
goals
02.
solution
03.
scope
04.
topics
05.
example
06.
process
07.
future
08.

## Slide 3: The playing field
The built environment
Program
Design
Build
End of Life
Built Environment
ComplexAsset
Asset
System
Space/Element
Component
Network/Collection
Asset Supply-Chain (SC) / Asset Breakdown
Asset Life-Cycle (LC)
Start of Life
Material
Operate*
* Including maintain, renovate and repurpose, demolish & recycle

## Slide 4: goals
Data integration
BIM standard
GIS standard
IoT standard
National regulation standard
Industry ‘standard’
Source: Jakob Beetz (2016)

## Slide 5: goals
Given meaning by distributed, linked ontologies*
* In NL often the term OTL – Object Type Library is used

## Slide 6: goals
Innovation example: predictive digital twin (DT)

## Slide 7: goals
Findable
  F1. (Meta)data are assigned a globally unique and persistent identifier
  F2. Data are described with rich metadata (defined by R1 below)
  F3. Metadata clearly and explicitly include the identifier of the data they describe
  F4. (Meta)data are registered or indexed in a searchable resource
Accessible
  A1. (Meta)data are retrievable by their identifier using a standardised communications protocol
  A1.1 The protocol is open, free, and universally implementable
  A1.2 The protocol allows for an authentication and authorisation procedure, where necessary
  A2. Metadata are accessible, even when the data are no longer available
Interoperable
  I1. (Meta)data use a formal, accessible, shared, and broadly applicable language for knowledge representation.
  I2. (Meta)data use vocabularies that follow FAIR principles
  I3. (Meta)data include qualified references to other (meta)data
Reusable
  R1. (Meta)data are richly described with a plurality of accurate and relevant attributes
  R1.1. (Meta)data are released with a clear and accessible data usage license
  R1.2. (Meta)data are associated with detailed provenance
  R1.3. (Meta)data meet domain-relevant community standards
FAIR data
Source: www.go-fair.org

## Slide 8
Passive Role (KM)
Active Role
W3C Linked Data & Semantic Web Technology
solution
R – Reusable
I - Interoperable
A - Accessible
F – Findable

## Slide 9: Solution
We need standards that support the application of that technology in industry
  Here: the built environment
Helping the information managers and modellers in practice
CEN TC442 (BIM) / WG4 (Support Data Dictionaries) /TG3 (Semantic Modelling and Linking) = prEN 17632
    Note: ‘Data Dictionary’ here to be interpreted as ‘Ontology’! (unhandy name like bSI bSDD)
But… Tech is not enough!

## Slide 10: solution
preEN 17632
Editorial Team
Benno Koehorst (RWS, NL) – Chair
Michel Böhms (TNO, NL) – Editor
Sara Asmussen (Leif Hansen Bygherrerådgivning, ISO 12006-3, GL)
Phil Jackson (University of Surrey, UK)
Davis Kantor (CRB, CH)
Ralf Klein (KU Leuven, BE)
Martin Schroeder (Bosch, DE)
Hugo Avalos (Knauf, DE)
Sanne Jansweijer (NEN, NL) – Secretariat
Paul van Rijsinge (NEN, NL) – Secretariat
Extended TG & external support/advice/inspiration
Espen Schulze (Cobuilder, NO)
Frédéric Grand (Cobuilder/bSI bSDD, NO)
Giorgio Schiavini (iBIMi, IT)
Vlad Nyvlt (Institute of Technology and Business , CZ)
Wolfgang Wilkes (University of Hagen, DE)
Sigve Pettersen (Fremby AS, NO)
Tim Lemoine (BBRI, BE)
Chi Ho Lau (bSI bSDD, NO)
Peter Muigg (CAD Anwendungen Muigg, AT)
Radboud Baayen (STABU, ISO 12006-3, NL)
Mick Baggen, Jaap Bakker (RWS, NL)
Daan Oostinga, Sander Stolk, Wouter Lubbers (Semmtech, NL)
Rik Opgenoort, Redmer Kronemeijer (CROW, NL)
Lucas Verhelst, Luuk Wijnholts, Miltos Gatzios (BIM Connected, NL)
Leo van Ruijven (Croonwolter en dros, NL)
Niels Hoffmann (Provincie Noord-Holland, NL)
Niels Reyngoud (Provincie Gelderland, NL)
Wouter van Riel (Infralytics, NL)
Dik Spekking (BIM Loket, NL)
René Wubbels (ProRail, NL)
Irene Polikof, Holger Knublaug, David Price (TQ, US)
Jan Voskuil (Taxonic, NL)
Berwich Sluer (Boskalis, NL)

## Slide 11: scope
Metalevels & language levels
L1:
information
language
L2:
Meta-
‘information
language’
M2: Meta-’information model’
M1: Information model
M0: Information set
of type
of type
of type
of type
of type
of type
of type
optional
optional
Top level information model
Information linking
: “some element in”
Information modelling

## Slide 12: scope
Data architecture for master data as specified by the ISO 8000 series
Ontologies
RDF, RDFS, OWL, SHACL, SKOS
URI
Strategy
Serialisation: XML, Turtle, JSON-LD, TriG, …

## Slide 13: scope
Use case types versus modelling power
Weak
semantic
modelling
Strong
semantic
modelling
LoC-1
Vocabulary/dictionary/
thesaurus
LoC-2
Basic ontology
LoC-3
Advanced ontology
OWL or
SHACL
RDF + SKOS
Data exchange
or sharing
Alignment of terms & definitions
Data
integration
RDFS only

## Slide 14: topics
Conceptual information language

## Slide 15: topics
To: RDF +
  SKOS
  RDFS
  OWL
  SHACL
Language bindings

## Slide 16: topics
Uri Strategy

## Slide 17: Topics
Combining languages
SKOS
RDFS
OWL
SHACL
C1 a rdfs:Class
T1 a skos:Concept
rdfs:seeAlso
skos:relatedMatch
T3 a skos:Concept
skos:definition
skos:prefLabel
skos:broader T2
skos:definition
skos:prefLabel
rdfs:subClassOf C2
P a rdf:Property
rdfs:domain
rdfs:range
P2 a rdf:Property
rdfs:subPropertyOf
C3 a rdfs:Class
rdfs:subClassOf
C1 a owl:Class
Restriction
(cardinality or value)
CX / CXShape sh:NodeShape’s
sh:Property
sh:Property
sh:Property
sh:Property (complex/extra)
P a owl:ObjectProperty
Union-domain
delivers
delivers
IMPORT
(NO IMPORT)
(weak linking)
EXTERNAL
sh:targetClass
sh:targetClass

## Slide 18: topics
Complex properties like complex quantities reusing QUDT
ex:Door_1
_:height1
ex:height
“2.4”
^^xsd:double
rdf:value
sml:
Quantity
Value
unit:M
sml:hasUnit
ex:Door
rdf:type
quantity
Kind:
Length
sml:hasQuantityKind
rdfs:range
owl:Object
Property
ex:height
rdf:type
rdf:type
(drived)
Implicit
in RDF

## Slide 19: topics
annotation

## Slide 20: Topics
Top level taxonomy
State
Event
hasState
triggers
hasState
triggers
begins
ends
hasPart
Temporal
Entity
Spatial
Entity
Activity
Information
Object
Physical
Object
hasPart
hasPart
isDescribedBy
hasInterior
hasBoundary
hasTemporalEntity
performs
transforms
transforms
hasState
triggers
Top
Concept
Concreet
Concept

## Slide 21: topics
Top level taxonomy – bit more precise
(W3C Time ontology)

## Slide 22: topics
Systems engineering

## Slide 23: topics
linking

## Slide 24: example
Modelling structures and their usage
Bridge
Deck
Slab
Vehicle
height
has legal speed
load level type
velocity
Non-geometric vehicle properties
{ … }
accuracy

## Slide 25: example
Coding according to SML

## Slide 26
process
10 june
21 october
~200 comments
processed
Benno Koehorst (RWS)

## Slide 27: future
Finish SML Part 1
Start SML Part 2: more domain-specific modelling patterns (PNWI), based on NEN 2660-2:
Industrial application, in NL alone:
  RWS AIRBIM RWS-OTL
  City of Amsterdam Engineering Dept.
  CROW BOR-OTL
  TenneT
  Province Gelderland
  Province Noord-Holland
  GWSW / GWSL
  CBNL, extending top level model like with “RoadNetwork”, “Building”, “Bridge”, “Tunnel”, …
  Pavement Information Model (PIM), Boskalis
  ….. many more
spatial regions versus real objects
materialization of physical objects (concrete, steel, asphalt, …)
interaction between objects including connections, interfaces and ports
requirements, unstructured and structured
  client needs
  laws and regulations
  sector recommendations
Implicit groups like “all main girders of a steel bridge”

## Slide 28: future
BIM and linked data coming together
©

## Slide 29: future
buildingSmart (bSI)
  IFC, ifcOWL, ifcJSON
bSI bSDD (in ISO 12006-3, JSON ?)
W3C RDF-star, Turtle-star, SPARQL-star (‘triple as subject’), compare LPGs
W3C LBD BOT ontology (“lightweight IFC-LD”)
  Check out: https://github.com/LBDserver by Jyrki Oraskari
ISO ICDD
  Packaging docs incl. LD docs
  Itself LD-based (meta-level)
CEN TC442 WG4 Data Template
  “Attributes for properties”
  Implemented in ‘ISO 12006-3 Revised’
Potential ingredients
Note
JSON-LD can be a common denominator:
W3C LD/SW
WebDev
?bSI (now JSON)

## Slide 30: future
CEN TC442 internal alignment
  “Data Templates”
  “Attributes for properties”
  Implemented in ‘ISO 12006-3 Revised’
  SML: + implemented in W3C LD/SW
  IFC-based data sets
  SML: + W3C LD/SW-based data sets

## Slide 31: future
CEN TC442 internal alignment – current positioning

## Slide 32: future
Much More to be done … in ISO 19650-speak:

## Slide 33: future
GitHub - buildingSMART/bSDD: bSDD development repo
Bsi bSDD json experiments /1
Database: import & output

## Slide 34: future
RDFS + SHACL
Bsi bSDD json experiments /2

## Slide 35: future
Need for harmonization!
ISO 12006-3:2021 is NOT bSDD JSON conceptually!
Step 1: Good 12006-3:2021-LD variant
Step 2: harmonize with bSI
Bsi bSDD json experiments /3

## Slide 36
Thank you for
your time